## Slide 1: ME 251
Anupam Saxena
Professor
Mechanical Engineering
Compliant and Robotic Systems Lab
Indian Institute of Technology Kanpur

## Slide 2
Feed Check Valve
Prepared by Anupam Saxena, Vitthal Khatik and Ishu Agrawal
NO. | PART | MATERIAL | QTY
1 | BODY | CI | 1
2 | COVER | CI | 1
3 | SPINDLE | MS | 1
4 | VALVE | GM | 1
5 | VALVE SEAT | GM | 1
6 | GLAND | GM | 1
7 | HAND WHEEL | CI | 1
8 | STUD | MS | 6
9 | STUD | MS | 2
10 | NUT | MS | 6
11 | NUT | MS | 3
PART LIST

## Slide 3
Feed Check Valve
Prepared by Anupam Saxena, Vitthal Khatik and Ishu Agrawal
NO. | PART | MATERIAL | QTY
1 | BODY | CI | 1
2 | COVER | CI | 1
3 | SPINDLE | MS | 1
4 | VALVE | GM | 1
5 | VALVE SEAT | GM | 1
6 | GLAND | GM | 1
7 | HAND WHEEL | CI | 1
8 | STUD | MS | 6
9 | STUD | MS | 2
10 | NUT | MS | 6
11 | NUT | MS | 3
PART LIST

## Slide 4
Feed Check Valve
Prepared by Anupam Saxena, Vitthal Khatik and Ishu Agrawal
NO. | PART | MATERIAL | QTY
1 | BODY | CI | 1
2 | COVER | CI | 1
3 | SPINDLE | MS | 1
4 | VALVE | GM | 1
5 | VALVE SEAT | GM | 1
6 | GLAND | GM | 1
7 | HAND WHEEL | CI | 1
8 | STUD | MS | 6
9 | STUD | MS | 2
10 | NUT | MS | 6
11 | NUT | MS | 3
PART LIST

## Slide 5
THREADED FASTENERS
Engineering systems are composed of parts which are joined together
Methods of joining
  Welding
  Riveting
  Adhesive bonding
  Using threaded fasteners

## Slide 6
Threads
  Helical feature made on the outer surface of a cylindrical part
THREADED FASTENERS

## Slide 7
Major diameter
Pitch diameter
Minor or root diameter
Pitch
Thread angle
Crest
Root
Flank
Chamfer
Pitch is distance measured parallel to axis between corresponding points on adjacent threads
THREADED FASTENERS

## Slide 8: Standard ISO Metric thread profile
Major diameter
Pitch diameter
Minor diameter
Pitch
R=H/6
THREADED FASTENERS

## Slide 9: Other Thread Profiles
White worth
ACME
Worm
Square
Buttress
Sharp V
THREADED FASTENERS

## Slide 10: Why so many profiles?
V threads:
  Large flank area and hence more friction. Used in effective positioning
  Difficult to make. Relatively weak
Whiteworh thread: Radius at crest and root reduces stress concentration
Square thread:
  Good for power transmission
  Flanks are perpendicular to thread axis allowing high load capacity
ACME thread: More stronger than square thread and easier to cut compared to square thread
Buttress thread: Used for transmitting power in one direction
Worm: Used in power transmission with speed reduction
THREADED FASTENERS

## Slide 11: Single start and Multi-start threads
Used when fast action is required
Single start
Double start
Triple start
THREADED FASTENERS

## Slide 12: Left and Right hand threads
Left hand
THREADED FASTENERS

## Slide 13: Thread designation
M 16 x 1.5 8 g LH DOUBLE
Number of starts
Metric thread
Major diameter (mm)
Pitch (mm)
Fine & Course
Bolt grade
Tolerance
Hand or Helix
THREADED FASTENERS

## Slide 14
Thread Designation
M10 × 1.25 – METRIC thread of nominal diameter 10 mm and pitch 1.25 mm
SQ 40 × 10 – SQUARE thread of nominal diameter 40 mm and pitch 10 mm
ACME 40 × 8 – ACME thread of nominal diameter 40 mm and pitch 8 mm
WORM 40 × 10 – WORM thread of nominal diameter 40 mm and pitch 10 mm
THREADED FASTENERS

## Slide 15: Conventional representation of threads in drawings
The distance between the line representing crest and root should be close to the actual distance but not less than 0.7 mm
In the sectional view, the hatching lines should extend till the crest of the thread
Crest (LT-A)
Root (LT-B)
Root (LT-B) represented by Partial circle
Visible threads
Sectional front view
Hidden threads
THREADED FASTENERS

## Slide 16: Schematic representation of V threads in drawings
Gives more details than the simplified representation
Used only for visible external threads or sectional view of internal threads- hatching ends at the root line in sectional view
Visible threads
Sectional view of internal threads
THREADED FASTENERS

## Slide 17: Schematic representation of square threads
Note the hatching in the sectional view
Visible threads
Sectional view of internal threads
THREADED FASTENERS

## Slide 18: Representation of threads in an Assembly
Bolts and threads are not sectioned in a sectional view
THREADED FASTENERS

## Slide 19
L
2D
D
0.75 D
R=1.5D
D
30o
D
2D
THREADED FASTENERS
Bolts and nuts- size and proportions

## Slide 20: Drawing a hexagonal nut
R=1.5D
2D
D
D
THREADED FASTENERS

## Slide 21
Source: https://donyango.carbonmade.com/projects/4388020

## Slide 22
CAR JACK ASSEMBLY
900
φ20
THREADED FASTENERS
LEAD SCREW
ACTUAL
ACTUAL and SCHEMATIC overlapped
H = 0.5P
P
H
H
H
L
L=P
D

## Slide 23
Source: https://donyango.carbonmade.com/projects/4388020

## Slide 24
Source: https://donyango.carbonmade.com/projects/4388020

## Slide 25
5
10
60
70
100
120
180
300
4 X R100
80
5
BASE
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 26
250
HANDLE
φ10
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 27
LOWER CHANNEL
250
220
5
45
50
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 28
SCREW RIGID CONNECTION
57.5
45
20
Ø20
15
10
62.5
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 29
SCREW THROUGH CONNECTION
12.5
20.0
15.0
10.0
61.5
Ø25.0
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 30
UPPER CHANNEL
250
2 X R12.5
2 X φ10
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 31
4 X Ø10
40
22.5
35
160
40
120
5
50
UPPER DECK
CAR JACK ASSEMBLY
THREADED FASTENERS

## Slide 32
THREADED FASTENERS