## Slide 1: ME 251
Anupam Saxena
Professor
Mechanical Engineering
Compliant and Robotic Systems Lab
Indian Institute of Technology Kanpur

## Slide 2
      Couplings
      used to directly transfer rotary motion from one shaft to another
      Types
        Fast or rigid coupling
        Flexible coupling
        Loose or disengaging (clutch)
COUPLINGS

## Slide 3: Rigid Coupling
Types
Muff Coupling
Flanged Coupling
Rigid shaft couplings
used for connecting shafts having collinear axes
COUPLINGS

## Slide 4: Butt muff coupling (rigid type)
COUPLINGS
https://grabcad.com/library/butt-muff-coupling-1
Machine drawing by K L Narayana, P kannaiah and V reddy
the ends of the two shafts to be coupled butt against each other, with the sleeve keyed to them

## Slide 5
Half-lap muff coupling (rigid type)
COUPLINGS
https://grabcad.com/library/half-lap-muff-coupling
Machine drawing by K L Narayana, P kannaiah and V reddy
The taper in the shaft ends prevent them from axially separating
Good for situations involving large axial loads

## Slide 6: Split muff coupling (rigid type)
https://www.stlfinder.com/model/split-muff-coupling-52587/1964005
https://www.learnpick.in/prime/documents/ppts/details/167/design-shaft-couplings
COUPLINGS
The muff is made in two semi-cylindrical halves joined together by bolts
Keys are placed in position then the muff is assembled
Torque is transmitted by key as well as by clamping friction
Used in heavy duty applications

## Slide 7: Flanged coupling (rigid type)
http://marineengineersblogs.blogspot.com/2013/06/types-of-coupling_17.html
Machine drawing by K L Narayana, P kannaiah and V reddy
COUPLINGS
Flanges are either fit or provided at the ends of shafts.
They are fastened together through a number of bolts and nuts.

## Slide 8: Flexible Coupling
Types
Bushed Pin Type Flanged Coupling
Compression Coupling
These permit relative rotation or variation in the alignment of shaft axes within certain limits.
COUPLINGS

## Slide 9: Bushed Pin Type Flanged Coupling (Flexible type)
COUPLINGS
Modified version of a protected flanged coupling
The flexible medium takes care of misalignment and acts as a shock absorber.
Used to connect prime mover or an electric motor and a centrifugal pump.
Image taken from Machine Drawing by Dr. K L Narayan,Dr. P. Kannaiah, K. Venkata Reddy

## Slide 10: Compression Coupling (Flexible type)
This coupling takes care of both axial and angular misalignment of shafts.
Friction between the shafts and sleeve assists in power transmission.
Image taken from Machine Drawing by Dr. K L Narayan,Dr. P. Kannaiah, K. Venkata Reddy
COUPLINGS

## Slide 11: Disengaging Coupling
Disengaging couplings are used when power transmission from one shaft to another is intermittent.
A dis-engaging coupling in general consists of one part firmly fixed to the driving shaft and another one mounted with provision for sliding over the driven shaft.
Types
Claw Coupling
Cone Coupling
COUPLINGS

## Slide 12: Claw coupling (clutch type)
https://grabcad.com/library/claw-coupling
Machine drawing by K L Narayana, P kannaiah and V reddy
COUPLINGS
Each flange has a number of identical claws which engage into the corresponding recesses in the flange.
One flange is firmly fit to the driving shaft through a taper sunk key and the other is placed over the driven shaft by two feather keys, so that it can slide freely on it.

## Slide 13: Conical Friction coupling (clutch type)
https://en.wikipedia.org/wiki/Cone_clutch
Machine drawing by K L Narayana, P kannaiah and V reddy
COUPLINGS
Two shafts may be coupled together via two flanges with conical surfaces (on the inside of one and on the outside of the other) by virtue of friction

## Slide 14: Non Aligned Couplings
Non-aligned couplings
transmit power between two shafts which are not coaxial.
Examples
Universal Coupling (Hooke’s Joint)
Oldham Coupling
COUPLINGS

## Slide 15: Universal Coupling (Hooke’s Joint)
https://www.google.com/search?q=universal+coupling&client=firefox-b-ab&source=lnms&tbm=isch&sa=X&ved=0ahUKEwj-npL1przbAhVDwI8KHfMfDkAQ_AUICigB&biw=1280&bih=621#imgrc=E8RxiaauXIyZbM:
http://mechteacher.com/universal-joint/
It is a rigid coupling that connects two shafts, whose axes intersect if extended.
The angle between the shafts may be varied even while the shafts are rotating.
Applications – Control Mechanisms, Tool Drives, Centrifugal Blowers.
COUPLINGS

## Slide 16
Image taken from Machine Drawing by Dr. K L Narayan,Dr. P. Kannaiah, K. Venkata Reddy
COUPLINGS
Universal Coupling (cont..)

## Slide 17: Oldham Coupling
It is used to connect two parallel shafts whose axes are at a small distance apart.
Power transmission takes place between the shafts, because of the positive connection between the flanges and the central disc.
Exploded View
Assembled View
Source: https://www.traceparts.com/en/product/technische-antriebselemente-gmbh-germany-oldham-coupling?CatalogPath=TRACEPARTS%3ATP01003006002&Product=80-13122007-537900
COUPLINGS

## Slide 18: Oldham Coupling
Image taken from Machine Drawing by Dr. K L Narayan,Dr. P. Kannaiah, K. Venkata Reddy
COUPLINGS