AE-4 Introduction to Aircraft Structures

Practice Problems

Shearing Stresses in Thin Walled Slender Beams

6.1 A built-up beam with the cross section shown is subjected to a vertical shear force of 10000 in.-lb. The flange angles are steel (E = 30  106 psi) and the web is aluminum (E = 10  106 psi). Determine the shear stress at the center of the web.

6.2 The angle section shown is loaded by a vertical force of 10,000 lb through the shear center. Determine the shear stress at A.

6.3 Determine the shear center of the idealized section shown. The area of all longitudinals is 1 in2.

6.4 Determine the shear-flow distribution in the idealized section shown.

6.5 (a) Determine the shear-flow distribution for a 1000-lb shear force at the shear center of the idealized section shown. (b) Compute the horizontal location of the shear center.

6.6 An idealized section is subjected to a vertical shear force of 1000 lb, as shown. All longitudinals have an area of 1 in.2, and all webs are 0.01 in. thick. Determine the shear-flow distribution.

6.7 Determine the horizontal location of the shear center of the section in Prob.6.6.

6.8 Determine the shear flows and forces in the longitudinals at the large end of the tapered beam shown when the tip is subjected to a 5000 lb vertical shear force in the plane of symmetry. The areas of all longitudinals are 1 in2.

# Text boxes

Rivets

10

0.12

ey

1000 lb

1 in2

1 in2

2 in2

2 in2

Figure 4

1000 lb

30

2 in2

2 in2

1 in2

1 in2

A

5

Figure 6

1000 lb

30

ey

10

5000 lb

5

Figure 3

10

7

3

Figure 2

A

2

2

0.2

Figure 5

40

0.2

Figure 1

A=0.5 in2

z

y

0.5

20

0.04

0.04

0.03

0.05

5000 lb

50

40

30

10

20

20

Figure 7