AE 232 Aerospace Structures-I

Assignment No. 4

Bending and Extension of Beams

4.1 Find the bending stress at point A if the Z section is subjected to the bending moment shown. All dimensions are in inches. Do not idealize the sections.

4.2 The rectangular beam shown is subjected to a temperature change T = 10z2+ z3. Find the stress at points A and B if = 10-5 in. / (in.) (oF) and E = 107 psi. All dimensions are in inches.

4.3 A bimetallic strip is used in the thermostat, which controls the cabin temperature         in a manned space station. The element is of the size and materials shown. Find            the clearance d, which should be provided to have the contacts close for a            temperature variation of 10F if the strip is straight at 72F. For invar = 1.1      10-6 in. / (in.) (F), E = 21  106 psi; and for copper  = 9.5 10-6in. / (in.) (F), E = 17  106 psi. All dimensions are in inches.

4.4 The idealized fuselage section shown is subjected to a bending moment of 10-6 in –lb about a horizontal axis. The effective areas of the longitudinals and their coordinates are given in the following table. Find the stresses in the longitudinals. Note that the fuselage is symmetric about Z0 axis.

| Longitudinal | Ai in.2 | y0 in. | z0 in. |
| --- | --- | --- | --- |
| 1 | 1.0 | 0.0 | 60.0 |
| 2 | 0.8 | 14.0 | 56.0 |
| 3 | 0.8 | 20.0 | 46.0 |
| 4 | 0.8 | 24.0 | 35.0 |
| 5 | 0.9 | 26.0 | 24.0 |
| 6 | 1.0 | 27.0 | 12.0 |
| 7 | 1.0 | 24.0 | 4.0 |
| 8 | 1.5 | 15.0 | 0.0 |
| 9 | 1.0 | 0.0 | 0.0 |

4.5 A cantilevered Z-section beam with the cross section given in Prob. 6.1 is 10 in._lb long and is loaded by a vertical force of 300 lb at the tip. Determine the vertical and horizontal components of the tip deflection.

# Text boxes

M=5 x104 lb-in

0.2

0.2

0.4

0.8

0.4

0.2

A

T = 10 z2 + z3

1

10

y

z

x

B

z

A

Invar

Copper

3

0.01

0.24

0.01

d

d

9

8

7

6

5

4

3

2

1

y0

z0