## Slide 1: 7 Old and 7 new tools for quality assurance
Dr. Raghu Nandan Sengupta
Professor
Department of Industrial and Management Engineering
All figures are taken from(unless otherwise mentioned):
Introduction to Statistical process Control
Douglas. C Montgomery
6th Edition

## Slide 2: 7 Old tools for Quality Assurance
A comprehensive statistical process control system uses seven tools to reduce variability and eliminate waste
  1. Histogram or stem-and-leaf plot
  2. Check sheet
  3. Pareto chart
  4. Cause-and-effect diagram
  5. Defect concentration diagram
  6. Scatter diagram
  7. Control chart(this will be discussed separately in greater detail in the next module of this course)

## Slide 3: Stem and Leaf Plot
Graphical representation of data
Let there be a set of 9 numbers {101,102,103,104,105,106,107,108,109}
To construct a stem and leaf plot, the numbers are divided into two parts – the stem and the leaves
Here the stem will be 10 and leaves will be {1,2,3,4,5,6,7,8,9}
Generally number of stems should be less

## Slide 4: Stem and Leaf Plot
Above example is ordered which makes it easy to find out the percentiles
the 100 kth percentile is a value such that at least 100 k% of the data values are at or below this value and at least 100 (1 − k)% of the data values are at or above this value

## Slide 5: Histogram
Continuous data is divided into intervals which are called class intervals, cells or bins
The number of bins does not have any agreed rule
  One heuristic is h=1+log2n where n=sample size and h= number of bins
Gives a visual impression of the shape of the distribution of the measurements and some information about the inherent variability in the data
Histogram is best suited for larger data sets containing, say, 75 to 100 or more observations
  Choice of number of bins becomes less influential in determining the shape of the distribution

## Slide 6: Histogram – An Example

## Slide 7: Check Sheet
Measure of DMAIC – collection of data
Check sheet is used to collect data in an organized way
Specify the type of data to be collected, the part or operation number, the date, the analyst, and any other information useful in diagnosing the cause of poor performance
A trial run to validate the check sheet layout and design

## Slide 8: A Check Sheet to Record Defects in Aerospace
Time-oriented summary is particularly valuable in looking for trends or other meaningful patterns

## Slide 9: Pareto Chart
A frequency distribution (or histogram) of attribute data arranged by category
Used both in Measure and Analyze step of DMAIC

## Slide 10: Pareto Chart
Pareto chart does not automatically identify the most important defects, but only the most frequent
When the list of defects contains a mixture of those that might have extremely serious consequences and others of much less importance, one of two methods can be used:
  Use a weighting scheme to modify the frequency counts.
  Accompany the frequency Pareto chart analysis with a cost or exposure Pareto chart

## Slide 11: Variations of Pareto Chart

## Slide 12: Cause and Effect Diagram
Once a problem has been identified, we have to look for possible sources of this problem
Cause and effect diagram is used in the analyze and improve steps of DMAIC to find potential causes
Also known as Ishikawa diagrams, these methods finds its application in both manufacturing and service industry
Several alternative classification methods of the causes

## Slide 13: Cause and Effect Diagram
5Ms used in manufacturing industry
  Machine(Technology), Method (process),Material (Includes Raw Material etc.), Man Power (Physical/mental work), Measurement (Inspection)
  Some people have included three more Ms
    Mother Nature, Management and Maintenance
8Ps used in marketing
  Product/Service, Price, Place, Promotion, People/personnel, Process, Physical Evidence, Packaging
5Ss used in the service industry
  Surroundings, Suppliers, Systems, Standard documentation skills, Scope of work

## Slide 14: Constructing a Cause and Effect Diagram

## Slide 15: Cause and Effect Diagram – An Example

## Slide 16: Defect Concentration Diagram
A defect concentration diagram is a picture of the unit, showing all relevant views
Then the various types of defects are drawn on the picture, and the diagram is analyzed to determine whether the location of the defects on the unit conveys any useful information about the potential causes of the defects.
Useful in the Analyze step if the DMAIC

## Slide 17: Defect Concentration Diagram

## Slide 18: Scatter diagram
Useful plot for identifying a potential relationship between two variables.
Let us say data is collected in pairs for two variables(x and y)
The shape of plot of y against x will give us some indication of relationship between x and y
Scatter diagrams are very useful in regression modelling
It must be kept in mind that scatter diagram gives potential relationship and not causality
  Designed Experiments may give us some causality

## Slide 19: Scatter Diagram – An example
The scatter diagram indicates a strong positive correlation between metal recovery and flux amount

## Slide 20: An Application of SPC
Improve quality and productivity in a copper plating operation at a printed circuit board fabrication facility
  High levels of defects such as brittle copper and copper voids and by long cycle time
Improvement team was formed
  Plating tank operator, the manufacturing engineer responsible for the process, and a quality engineer
Define
  Concentrate on reducing the flow time through the process, as the missed delivery targets were considered to be the most serious obstacle to improving productivity

## Slide 21: An Application of SPC
Measure
  Excessive downtime on the controller that regulated the copper concentration in the plating tank was a major factor in the excessive flow time; controller downtime translated directly into lost production
Analyze
  Brainstorming -> cause and Effect Diagram

## Slide 22: An Application of SPC
Data collection for controller downtime was necessary
  The cause and effect diagram was used to design the check sheet

## Slide 23: An Application of SPC
Based on the data Pareto charts were made

## Slide 24: 7 New tools for Quality Control
In 1976 the UJSW(Union of Japanese Scientists and Engineers) collected and promoted 7 Management and Planning(MP) tools
The 7 tools were
  Affinity Diagram
  Relations Diagram
  Tree Diagram
  Matrix Diagram
  Matrix Data Analysis(beyond the scope of broad discussion)
    Often replaced by prioritization matrix due to the complex mathematical nature
    A prioritization matrix is an L shaped matrix that uses pairwise comparison of a list of options to select criteria
  Arrow Diagram
  Process Decision and Program Chart

## Slide 25: Affinity Diagram
Also kwon as affinity chart, K-J method variation
When to use
  After a brainstorming session
  When analyzing verbal data such as survey
How to create one affinity diagram
  Record each idea with a marking pen on a separate sticky note or card.
  Look for ideas that seem to be related in some way. Place them side by side
  When ideas are grouped, select a heading for each group. Look for a note in each grouping that captures the meaning of the group.
  Combine groups into “supergroups” if appropriate

## Slide 26: An Application of SPC

## Slide 27: Relations Diagram
The relations diagram shows cause–and–effect relationships.
When to Use a Relations Diagram
  When trying to understand links between ideas or cause–and–effect relationships
  When a complex solution is being implemented.
  After generating an affinity diagram or cause and effect diagram
Basic Steps
  Write a statement defining the issue that the relations diagram will explore.
  Brainstorm ideas about the issue and write them on cards or notes
  Place one idea at a time on the work surface and ask: “Is this idea related to any others?”
  For each idea, ask, “Does this idea cause or influence any other idea?” Draw arrows if answer is yes.
  Analyze the diagram

## Slide 28: Relations Diagram
For source of image see reference

## Slide 29: Tree Diagram
The tree diagram starts with one item that branches into two or more, each of which may branch into two or more
It is used to break down broad categories into finer and finer levels of detail
When to Use a Tree Diagram
  When developing actions to carry out a solution or other plan
  When probing for the root cause of a problem.
  When evaluating implementation issues for several potential solutions.

## Slide 30: Tree Diagram
Procedure for a tree diagram
  Develop a statement of the goal, project, plan, problem or whatever is being studied. It is the first node.
  Ask a question that will lead you to the next level of detail
  Do a “necessary and sufficient” check for the level
  Each of the new idea statements now becomes the subject: a goal, objective or problem statement.
  Continue to turn each new idea into a subject statement and repeat the process
  Do a “necessary and sufficient” check of the entire diagram.

## Slide 31: Tree Diagram
For source of image see reference

## Slide 32: Matrix diagram
The matrix diagram shows the relationship between two, three or four groups of information
  Strength of relationship and roles played
When to use matrix diagrams
For source of image see reference

## Slide 33: L Shaped Matrix Diagram
For source of image see reference

## Slide 34: T Matrix Diagram
For source of image see reference

## Slide 35: Y Matrix Diagram
For source of image see reference

## Slide 36: Arrow Diagram
The arrow diagram shows the required order of tasks in a project or process
It can be used for:
  Determining best schedule for the entire project
  Potential scheduling and resource problems and their solutions.
  Calculate the critical path of the project
When to use an arrow diagram
  When scheduling and monitoring tasks within a complex project or process with interrelated tasks and resources.
  When you know the steps of the project or process, their sequence and how long each step takes
  When project schedule is critical, with serious consequences for completing the project late or significant advantage to completing the project early

## Slide 37: How to use an Arrow Diagram
List all the necessary tasks in the project or process
Determine the correct sequence of the tasks
  Create a table with four columns —prior tasks, this task, simultaneous tasks, following tasks.
Diagram the network of tasks.
  Time should flow from left to right and concurrent tasks should be vertically aligned.
Between each two tasks, draw circles for “events.”
Look for three common problem situations and redraw them using “dummies” or extra events

## Slide 38: When to use Dummy Events
Two simultaneous tasks start and end at the same events
  Use a dummy and an extra event to separate them
Task C cannot start until both tasks A and B are complete; a fourth task, D, cannot start until A is complete, but need not wait for B
  Use a dummy between the end of task A and the beginning of task C.
For source of image see reference
For source of image see reference

## Slide 39: Dummy Events
A second task can be started before part of a first task is done
  Add an extra event where the second task can begin and use multiple arrows to break the first task into two subtasks
For source of image see reference

## Slide 40: Arrow Diagram
When the network is correct, label all events in sequence with event numbers in the circles. It can be useful to label all tasks in sequence, using letters
Once this is completed CPM or critical path method can be used for scheduling the tasks
Let us look at some basic steps and terminology related to CPM

## Slide 41: Critical Path Method
Determine task times
Determine the “critical path,” the longest path from the beginning to the end of the project
  Length of the critical path: the sum of all the task times on the path.
Calculate the earliest times each task can start(Earliest Start ES) and finish(Earliest Finish EF), based on how long preceding tasks take
  Start with the first task, where ES = 0
  For subsequent tasks:
    ES=the largest EF of the tasks leading into this one
    EF=ES + task time for this task

## Slide 42: Critical Path Method
Calculate the latest times each task can start and finish without upsetting the project schedule, based on how long later tasks will take. These are called latest start (LS) and latest finish (LF).
  Start from the last task, where the latest finish is the project deadline, and work backwards
  Latest finish (LF) = the smallest LS of all tasks immediately following this one
  Latest start (LS) = LF – task time for this task
Calculate slack time for each task and project
  Total slack = LS – ES = LF – EF
  Free slack = the earliest ES of all tasks immediately following this one – EF

## Slide 43: Process Decision Program Chart
The process decision program chart (PDPC) systematically identifies what might go wrong in a plan under development.
When to use PDPC
  Before implementing a plan, especially when the plan is large and complex.
  When the plan must be completed on schedule.
  When the price of failure is high.
  When the project is identified as risky

## Slide 44: PDPC Procedure
Obtain or develop a tree diagram of the proposed plan
  High-level diagram showing the objective, a second level of main activities , third level of broadly defined tasks
For each task on the third level, brainstorm what could go wrong.
Review all the potential problems and eliminate any that are improbable or whose consequences would be insignificant.
For each potential problem, brainstorm possible countermeasures.
Decide how practical each countermeasure is.

## Slide 45: PDPC Example
For source of image see reference

## Slide 46: References
https://en.wikipedia.org/wiki/Ishikawa_diagram
http://asq.org/learn-about-quality/new-management-planning-tools/overview/overview.html
http://asq.org/learn-about-quality/idea-creation-tools/overview/affinity.html
http://asq.org/learn-about-quality/new-management-planning-tools/overview/tree-diagram.html
http://asq.org/learn-about-quality/new-management-planning-tools/overview/arrow-diagram.html
http://asq.org/learn-about-quality/new-management-planning-tools/overview/matrix-diagram.html
http://asq.org/learn-about-quality/new-management-planning-tools/overview/process-decision-program-chart.html