LECTURE 8

First Law Analysis to Non-flow Processes

Constant Volume process:

- Heating of gas enclosed in a rigid vessel:

dU = dQ or U2- U1 , Q = m Cv (T2 – T1)

- Shaft work done on a system at constant volume

dU = dQ- dW = dQ – (dWpdv + dWs)

or dU = - dWs or -Ws  = U2- U1

- Constant volume process involving electrical work:

- Ws  = U2- U1

For an adiabatic process the work is done is independent of path.

Constant Pressure Process

- Reversible heating of a gas

- Phase Change at constant pressure(Rev.)

- Shaft work at constant pressure

- Electrical work at constant pressure

W = P (V2 –V1)

dU = dQ-dW = dQ- PdV = dQ- d(PV)

or, dQ = dU + d(PV) = d(U+ PV) = dH

Q = (H the heat interaction is equal to increase in enthalpy

Constant Temperature Process

dU = dQ-dW = dQ- PdV

for an ideal gas u= u(T) then dU = 0

dQ = PdV = RT (dv/v)

Q = W = RT ln (v2/ v1)

Reversible Adiabatic Process

dU = -dW  or W = -(U

This equation is true for reversible as well as irreversible process.

Cv dT = -Pdv = -RT/v dv

dT/T = -R/Cv dv/v

R/Cv = ( - 1

dT/T = -((-1) dv/v

T2/T1 = (v1/v2) ((-1)   Tv((-1) = constant

Also Pv ( = Constant using perfect gas relation